## Slide 1: Open Frame Tablet ARM Embedded Solutions Department

## Slide 2
(picture from Google)

## Slide 3
Low cost & low power panel PC like tablet
Power on without battery
Fully flat touch screen
Slim design but with strength
Fit into any embedded applications
Compatible with multi-OS platform
Concept

## Slide 4
Open frame tablet

## Slide 5
(picture from Google)
Application

## Slide 7
Bay Trail T-CR Z3735F

## Slide 8
 | Intel ATOM Z3735F | Rockchip RK3188 | Freescale i.MX6Q
 | Quad core @ 1.33 GHz (Burst 1.83GHz) | Quad Core Cortex-A9 @ 1.6GHz | Quad Core Cortex-A9 @ 1.0GHz
Antutu 5.X |  |  | 
Overall | 29851 | 21900 | 11104
Multitask | 3947 | 4438 | 2049
Runtime | 2064 | 1352 | 713
RAM Ops | 2158 | 2303 | 1018
RAM Speed | 3281 | 1179 | 519
CPU Integer (multi-thread) | 3035 | 2048 | 938
CPU float-point (multi-thread) | 2984 | 2403 | 1098
CPU Integer (single thread) | 1572 | 1303 | 636
CPU float-point (single thread) | 1696 | 1450 | 693
2D Graphics (1920×1080) | 1346 | 1052 | 609
3D Graphics (1920×1080) | 5904 | 3013 | 312
Benchmark with ARM

## Slide 9
Intel E3845/
J1900
Intel
Z3735F
Freescale i.MX6Q
Low ------------ Cost ------------- High
Low ----- Performance ------ High
Cost-performance

## Slide 10: OFT-07W01 Feature
802.11 b/g/n WiFi
10/100 LAN Ethernet
12V to 19V DC input
Preboot eXecution Environment
Integrated antenna
1GB or 2GB RAM
8GB or 32GB eMMC

## Slide 11
Optional POE 802.3AT (10” only )
OFT-10/15/21W01 Feature
802.11 b/g/n WiFi
10/100 LAN Ethernet
12V to 19V DC input
Preboot eXecution Environment
Integrated antenna
2GB RAM
8GB or 32GB eMMC

## Slide 12
Panel |  |  |  | Touch |  | 
Size | Resolution | Luminance | View Angle (H+-)/ (V+-) | Touch | Bonding | Surface hardness
7" | 1280*800 | 300 | 165° (H/V) | PCAP | Air bonding | 6H
10.1" | 1280*800 | 350 | 170° (H/V) | PCAP | Air bonding | 6H
15.6" | 1920*1080 | 200 | 89°/89°/89°/89° | PCAP | OH-cell | 6H
21.5" | 1920*1080 | 250 | 178°(H/V) | PCAP | on-cell | 6H
4 Panel Size

## Slide 13
DC Jack
LAN Port
USB2.0*2
HDMI
Audio Jack
Micro SD
External IO

## Slide 14
RS485
Speaker
RS232
USB
A-MIC
GPIO
Touch
Button
DC input 4pin header
Internal IO

## Slide 15
Placement

## Slide 16
Front view
Back Mounting Design
Side view
Example:10W01

## Slide 17
Back view
Back Mounting Design
Example:10W01

## Slide 18
Wall
Wall box
Panel bracket
OFT-10W01
Front bezel
Wall mount
Reference Design 1

## Slide 19
Customization fixture
Wall
OFT-10W01 with front bezel
Wall box
Wall mount
Reference Design 1

## Slide 20
Wall
OFT-10W01 with front bezel
Wall box
Screw cover
Wall mount
Reference Design 2

## Slide 21
Wall
OFT-10W01 with front bezel
Wall box
Name plate
Wall mount
Reference Design 3

## Slide 23
Extended Bracket
*Bracket Sold Separately

## Slide 24
Front view
Front Mounting Design
*Bracket Sold Separately
Side view
Example:10W01

## Slide 25
Back view
Front Mounting Design
*Bracket Sold Separately
Example:10W01

## Slide 26
Chart: 
| Android | Windows | Linux
銷售 | 33.3 | 33.3 | 33.3
Ubuntu 14.04
Android 4.4
Windows 8.1
Windows 10
Multi-OS Compatibility

## Slide 28
1. Can memory size expand to 2GB above?
2GB
2. Does display support dual-display?
LCD + HDMI Windows/ Linux: extended mode Android: extended mode by APP
3. Can system support 64bit OS?
Android & Ubuntu
4. Can system support 32bit OS?
Windows
Q&A

## Slide 29
5. Which Android version is supported now?
Android 4.4 (Kernel 3.10)
6. How to update Android OS?
by SD card/ USB (OTA update)
  7. Which Linux distribution is supported now?
  Ubuntu 14.04 (Kernel 3.16)
  8. Can we provide Linux Kernel source code?
  provide kernel installation package (BSP)
9. Which Windows version could be pre-installed now?
  Windows 8.1/10 Embedded Industry retail (ePKEA)
Q&A

## Slide 30
10. What’s warranty period ?
12+3 months (extra 3 months for delivery/ warehouse)
11.What’s CPU life time guarantee?
3+2 years (2015~2018, extend to 2020)
Q&A

## Slide 32
USB 3.0
PCIe 2.0
2 Display Pipes
SDIO 3.0
Cherry Trail Z8300

## Slide 33
2015 Q4
7”/ 10”/15”/21”
Open Frame Tablet
with Bay Trail
2016 Q4
7”/ 10”/15”/21”
Open Frame Tablet
with Cherry Trail
Roadmap

## Slide 34
OFT-XXW02 Block Diagram

## Slide 35
OFT-XXW02 EVT Placement

## Slide 36
OFT-XXW02 EVT Placement

## Slide 37
OFT-XX02 Block Diagram

## Slide 38
OFT-XX02 EVT Placement